## Slide 1
Evaluation of Mother-Daughter Architectures for Asteroid Belt Exploration
Leonard Vance, Jekan Thanga, Erik Asphaug
University of Arizona
Notes: 1

## Slide 2: Over 700,000 asteroids are currently cataloged - Some as small as a few meters Each tracked asteroid represents a potentially large source of material for development. Low gravitational potential reduces the cost of visitation. We have little understanding of their individual composition
Large Binocular Telescope
Catalina Sky Survey

## Slide 3: Individual sample and return missions from a significant number of asteroids allows us to understand the statistical make-up of the belt, improving in-situ resource development.
OSIRIS-Rex Sample Return Mission to to Near Earth Asteroid Bennu
Bennu

## Slide 4
MotherShip Trajectory
Solar System
Question:
How effectively can a nano-spacecraft swarm explore the asteroid belt when limited to a 2 year lifespan?
2) Brake
3) Return
4) Return Brake
Nano-Spacecraft
1) Intercept
To Other
Asteroids
MotherShip
Asteroid
2 Year Mission Maximum
Mission Overview:
Multiple Nano-spacecraft are deployed from a mothership within the asteroid belt, each executing a sample and return from a known asteroid.

## Slide 5
Example: 300 m/s Initial burn
1 year orbital propagation
14 asteroids within resulting volume
Inner Solar System
Mother ship in median asteroid belt
Maneuver Boundary
Intercept Potential is established by determining inclusion within a nano-spacecraft maneuver boundary
Multiple intercepts appear possible even using a small delta-V within the limited lifespan of a Nano-satellite
Next Question: What does an optimal initial orbit look like?

## Slide 6
Asteroid Density in Solar System
Jupiter Orbit
Median Asteroid Orbit
Asteroids inside an annulus with 6.46x106 Km radius and specified radius from sun
Chosen Altitude for Exploration
3.95x1011 m
Density afo Distance from Sun
Place nominal mothership orbit at the location of highest asteroid density

## Slide 7
Many asteroids can be reached as nano-spacecraft flyout time increases
Orbit Radius = 3.95x1011 m
Mothership Mean Anomaly = 0
Inclination = 0 deg
Hundreds of asteroids can be reached given reasonable delta-Vs and flyout times
Next Question: How much delta-V does it then take to stop and return to the mothership?

## Slide 8
Asteroid entering kinematic boundary
Min. Delta-V to Intercept
1500m/s limit imposed on intercept
3000m/s limit imposed after braking to halt
Minimum Sample and Return Delta-V
In this epoch
Overview of Nano-Spacecraft Delta-V components for Asteroid Sample and Return
Combining elements of the sample and return flight provides an initial assessment of the total Delta-V necessary

## Slide 9
Number of viable missions rise quickly as nano-spacecraft delta-V increases above 2000m/s
Nominal Baseline
(2500 m/s)
A cutoff at 2500 m/s total mission delta-V provides 23 mission opportunities
Nano-spacecraft limited to 2 year lifespan

## Slide 10
Mission Example:
2 year lifespan limit
2.5 km/s delta-V per spacecraft
Mothership in median Asteroid orbit (yellow)
All nanospacecraft launched at beginning of epoch (Blue)
All nanospacecraft return at two years
23 Asteroids sampled

## Slide 11
Choice of initial orbit anomaly can significantly effect mission opportunities
mothership initial mean anomaly
Range of available potential sample and return missions
A factor of two difference depending upon the choice of initial phase of orbit.
2 year lifetime assumed

## Slide 12
Process:
Sample random asteroid pairs
Throw out pairs which are more than 1 AU apart
Bootstrap until 500,000 pairs are selected
Use conventional Computation to calculate sample and return Delta V for each of those 500,000 pairs
Provide this database as input to a Neural Net for supervised training
Run trades on number of hidden layers and nodes in each layer to establish best performance
Establishing number of missions for each location is computationally intensive
    - Only 8 points derived for 6 hours of CPU work
Use of a neural network to approximate delta-V calculations could significantly improve speed
Optimization of Number of Nodes for a 3 layer Configuration

## Slide 13
12
Input
w
b
+
Hidden Layer 1
18
TanSig
w
b
+
Hidden Layer 1
9
TanSig
w
b
+
Hidden Layer 1
14
TanSig
1
Output
The chosen 3 layer configuration provides a respectable estimate of sample and return delta-V
Training Error History
Actual vs. Estimated Delta-V
a = tansig(n) = 2/(1+exp(-2*n))-1

## Slide 14
Heliocentric Y coordinate (AU)
Heliocentric X coordinate (AU)
Sample and Return Missions Available
# of Available missions
Max = 766
Neural Network Delta-V approach increases calculation speed by over 1000x
Sample and Return opportunities from a Mothership can now be mapped over the entire solar system
2 year nano-spacecraft lifetime
5 km/s delta-V per spacecraft
Assume mothership circular orbit
Julian epoch 2458200.5 (March 2018)

## Slide 15: Conclusions and Summary
The large number of tracked asteroids suggests use of swarms for exploration
The Delta-V required to enable large scale sample and return from a single mothership is approximately 2.5 km/s
A two year nano-spacecraft lifespan is adequate for this approach
Large scale sample and return exploration of asteroids is plausible with nano-spacecraft utilizing single stage propulsion