## Slide 1: Mars Small Spacecraft The opportunity of the roaring 20ties
Vlada Stamenkovic, C. D. Edwards, N. J. Barba, R. C. Woolley, L. Giersch, T. A. Komarek, V. Cormarkovic, P. E. Clark, A. Chmielewski,
et al.
Jet Propulsion Laboratory, California Institute of Technology

## Slide 2
How to do it small?
What mission concepts?
What science?
Why Mars?
Last thoughts & summary

## Slide 3
How to do it small?
What mission concepts?
What science?
Why Mars?
Last thoughts & summary

## Slide 4
P = 6 mbar
T = 140-300
fO2 = 0.146 %
Organics being destroyed on the surface
Mars today…been there, done that?

## Slide 5: BUT…whiffs of weird gases…
Giuranna + 2019
Methane?
5
Oxygen?
Trainer + 2019
Webster + 2018
“The mysterious appearance and disappearance of methane in the Martian atmosphere remains the most compelling hint of possible life in the subsurface of Mars,”
Dr. Pratt (NASA PP).
Trainer + 2019

## Slide 6
Hidden diversity below…power to fuel life?
Redox gradients with depth?
Eigenbrode + 2018
Where is the organics coming from?

## Slide 7: A refresher…young water?
Young Outflow Channels in Athabasca and Kasei
[Burr et al., 2002; Chapman et al., 2010]
Aquifer or juvenile water?
Orosei + 2018
Liquid (ground)water today?

## Slide 8
P = 6 mbar
T = 140-300
fO2 = 0.146 %
Organics being destroyed on the surface
Mars today…been there, done that?

## Slide 9: Been there…but haven’t done that!
Big, game-changing, Mars questions left unanswered.
Orosei + 2018
Eigenbrode + 2018
Webster + 2015, 2018
Trainer + 2019
Water?
Organics?
Power to fuel life?
Trace Gases?
Climate record?

## Slide 10: MEPAG changes: subsurface & extant life
These questions reflect recent (March 2020) changes in the MEPAG documents, especially to Goal I (Life).
Back to life, into the deep  tight new bonds to Ocean Worlds & Human Exploration

## Slide 11: Planned Mars Sample Return Campaign
We need to find affordable options!
$$$

## Slide 12
How to do it small?
What mission concepts?
What science?
Why Mars?
Last thoughts & summary

## Slide 13: Small Spacecraft is the solution
Small spacecraft can provide low cost access to compelling science investigations at Mars.
From Mars orbit to the Martian surface/subsurface (the latter being key).
Orbiter
Surface
& Subsurface
Solution
Technically Feasible
Mars small spacecraft can meet mass/volume constraints that allow reaching Mars via “rideshare” launches to GTO and/or new classes of small commercial launch vehicles.
Low Cost
Mars small spacecraft can get to Mars for costs of ~$100M - 300M including phases A to D and the launch costs.
Scientifically Compelling
Mars small spacecraft can accomplish decadal class science while being complementary to Flagship missions in type of science investigation.

## Slide 14: Three Key Methods to Get Small Spacecraft to Mars
Piggyback to Mars
  Pro: Cheap, direct delivery
  Con: Few reliable options
Earth Rideshare + Propulsion
  Pro: Cheap, lots of options
  Con: Secondary, need propulsion
Dedicated Launch
  Pro: Custom, full control
  Con: Kick stage, low TRL
Flyby or
MOI
MarCO
DS2 1999
MarCo 2018
M2020 (2020)
Psyche FB (2022)
MSR (2026?)
IceMapper (2026?)
Beyond???
ESPA
Ring
Primary
LV Adapter
Many small LVs are in development with > 1000 kg to LEO . Firefly + solid motor would be capable to reach Mars. Others may follow.
Mass: varies
Frequency: > 2 years
Mass: 100-400 kg
Frequency: > 6 per yr
Mass: 100-300 kg
Frequency: 2021+
Can be used with EP
for delivery to orbit, or ballistically for direct entry
Firefly Alpha
Notes: Piggyback
  Release after launch
  Release prior to arrival
  (Not included in the chart - for landers) Release during EDL or after landing – these devices should be considered “detachable instruments”.
Small launch vehicle + a solid motor. So far Firefly is the only one that seems to be capable to lift about 1000 kg to LEO, or with a STAR30 about 200 kg to Mars. But there are other emerging small LVs such as RocketLabs, VOX/Virgin, Astra, et al. Firefly status: We visited Firefly in September. CDR planned in January, USAF and NASA/LSP are invited. Funded through the 1st launch planned for end on 2019.
Rideshare 2ndary P/L on ESPA – the most promising option

## Slide 15: Promising Small Launch Vehicles for Mars
Company | Rocket | Cost | 1st Launch | Fairing | LEO | Mars Entry* | LMO* (w/ AB)
FireFly | Alpha | $15M | late 2019 | 2.0 | 1000 kg | 200kg | 130 kg
Relativity Space | Terran 1 | $10M | late 2020 | 1.9 | 1250 kg | 250 kg | 160 kg
ABL Space | RS1 | $12M | late 2020 | 1.8 | 1200 kg | 240 kg | 150 kg
Lunette Concept (2009)
Star 27, 2 km/s LOI
*Additional “kick” stage required for Trans-Mars Injection
Assumptions
Use STAR 30E kick stage
May need to be stretched
20 kg for adapter
300 km LMO uses biprop to 24hr orbit
6 mos. for aerobraking

## Slide 16: Path to Mars Orbit Via Rideshare
2.8 +/- 0.7 km/s
770 m/s
LV “Disposal”?
LV
Chemical
SEP
GTO
C3=0 (escape)
5.7 km/s
350-600 days
200 - 500 days
Vinf = 0 (capture)
Deimos (20,000 km)
Areo (17,000 km)
Phobos (6,000 km)
1 km/s
1-1.5 km/s
30-80 days
80-200 days
LMO (300 km)
2.5 – 3.3 km/s
200 - 400 days
~1200 m/s
C3 ~ 10
Vinf ~ 3
2300 m/s
SEP delivers ~60% more mass to High Mars Orbit
Rigid constraints on date and orientation!
Inclination constraints
Areo
1900+ m/s
Incl. plane change and orbit transfers
1200 m/s*
*Includes ~6 months aerobraking
GTO
Ballistic Coast
A possible Lunar gravity assist Flyby may save about 1 km/s. Not included in the baseline.
SEP Delta V ~ 9.5 km/s
Notes: Notes:
ΔV’s are approximate; ΔV’s don’t necessarily add, especially with SEP; SEP ΔV’s based on 300 kg and 45 mN
Most values require proper Earth-Mars alignment (i.e. Launch/arrival dates)
Positive C3 departures require correct asymptote (i.e. stringent constraints on the launch geometry), C3=0 does not

## Slide 17: MaSMi (AXE) Interplanetary EP Thruster
MaSMi thruster ideally suited for small EP missions to Mars
  Magnetically Shielded Miniature Hall Thruster
  Developed and tested at JPL
  Recently licensed to Apollo Fusion for production (labeled Apollo Xenon Engine or AXE)
Shielding  10x lifetime vs. conventional Hall
Max Power | 1075 W
Min Power | 160 W
Isp | 1935 s
Thrust | 69 mN
Efficiency | 51%
Lifetime: 10,000+ hrs
Production: 2020
Mass: < 5 kg
Xenon: 200+ kg

## Slide 18
How to do it small?
What mission concepts?
What science?
Why Mars?
Last thoughts & summary

## Slide 19: Compelling Science from Small Spacecraft
Fundamental & New Single Measurements
3D/4D is the Science
Global Coverage
Networks
Causality
Processes
Scouts
Targeted Science
One instrument drives all.
Special Landing Zones are Enabled
High value science at low cost, complementary to MSR.
Notes: Note: add a MEPAG goals matrix/HEO SKGs  update for small s/c

## Slide 20: Compelling Science from Small Spacecraft
Groundwater; EM Fields; H2O/CO2 Condensation at Poles; Subsurface Redox Profiles; Exogenic Influx; etc.
High Resolution Imaging (Visual, IR, Spectroscopic) for landing site selection and reconnaissance; Exogenic Influx & Chemistry; Trace Gas Sinks, Sources, and Transport; Groundwater, etc.
Atmospheric Erosion Drivers; Trace Gas Sinks, Sources, and Transport; Weather Dynamics; Wind Dynamics; Dust & Aeolian Dynamics; Surface-Subsurface Exchange of Vapor Dynamics/Transport.
3D Seismology; 3D Radar; EM Propagation, etc.
Special Locations, such as Poles, Valles Marineris, Southern Highlands, Lowest Altitude, Caves, etc.
Fundamental & New Single Measurements
3D/4D is the Science
Global Coverage
Networks
Causality
Processes
Scouts
Targeted Science
One instrument drives all.
Special Landing Zones are Enabled
High value science at low cost, complementary to MSR.
Notes: NOTE: 3D can be done from orbit with one asset.
3 landed assets can cost up to 200 M.

## Slide 21
How to do it small?
What mission concepts?
What science?
Why Mars?
Last thoughts & summary

## Slide 22: Compelling Smallsat Science From Orbit and On the Surface
Methane?
Organics?
Webster et al. (2018), Science
Eigenbrode et al. (2018), Science
Organic Matter at Gale Crater
Areostationary
Groundwater?
4D: Trace gas sniffers
Orosei et al. (2018), Science
Scouts?
Low orbit
Recon
Notes: Note: add a MEPAG goals matrix/HEO SKGs  update for small s/c

## Slide 23: Find the water with SHIELD & TH2OR!
PURE WATER IN THE TROPICS ~2-6 km depth
Groundwater Table Depth [km]
VALKYRIE proposal, Stamenkovic + 2019

## Slide 24: Find the water with SHIELD & TH2OR!
Challenge: Is there liquid water on Mars? What is its composition? Could this be a modern habitat?
Objectives: Demonstrate that we can uniquely sound from the Martian surface for groundwater, expected to be at depths of kilometers, using a low-mass (<5-10 kg) and low-power (<10-100 W average) EM system and to determine its salinity.
 | Earth | Mars
Typical crustal conductivity | 10-2 S/m | 10-7 S/m
Ocean water | 1 S/m | 
Contrast | ~102 | ~107
Mars is ideal for TEM groundwater search:

## Slide 25
SHIELD enables the transportation of small scientific payloads affordably to the surface.
Landed Mass: 50kg
Science Payload Mass: 6kg
Impact load range 1000 g – 2000 g.
Static science platform, options for surface and aerial mobility.
Target mission duration: 90 sols to 1 Martian year (latitude dependent)
Low Cost Approach
Hosted, secondary, or dedicated P/L configurations.
No parachute or propulsive deceleration. Low ballistic coefficient to slow down.
Science Objective:
Subsurface liquid water detection using transient electromagnetic sounder.
Primary Instrument:
TH2OR TEM Liquid Sounder; 100 m transmit loop, receive loop, detector electronics.
Secondary Instrument:
Meteorological sensors, trace gas sensors, dust sensors, and/or imager(s). Ruggedized for impact and environment
Mission Duration:
Primary -1 month, Extended -1 Mars year
Configuration:
Multiple SHIELD landers with cruise stage
Mission Design:
Ballistic trajectory, landing at equator +/- 30° latitude
TH2OR Mission Concept
25
5/10/20
Pre-decisional. For planning and discussion only.
© 2020. California Institute of Technology. Government sponsorship acknowledged.
Find the water with SHIELD & TH2OR!

## Slide 26: Find the source of organics
LOKI (Localizing Organic Key Ingredients)
LOKI
Organics, exogenic or endogenic?
Ground CH4, O2 data in 4D.
Science Goal:
Measure exogenic organic influx.
Measure atmospheric CH4/O2/H2O/H2O2 variability on the surface.
Surface Instruments:
Mini-TLS [2 (CH4 and H2O)-4 channels (+O2, H2O2)]
Orbiting Instrument:
Widefield camera with appropriate filter (likely UV).
Mission Duration:
Primary: 1 Mars year, Extended: 2 Mars Years
Configuration:
One SHIELD lander with cruise stage, cruise stage stays in orbit as mothership
Mission Design:
Ballistic trajectory
Landing at equator +/- 30° latitude
Orbit areostationary
Localize the sources and sinks for methane and organics on Mars.
Science Objectives:

## Slide 27: Global Monitoring & 4D science The Example of Areo-TGL
Mass: ~190 kg dry mass
Target: Mars – Areostationary Orbit
Instrument: Spacial Heterodyne Spect.
Configuration: Single s/c, constellation
Launch: Secondary P/L on ESPA Grande
Cruise: Solar electric propulsion
Risk Class: D
Lifetime: ~3 years in orbit then replenished
Telecom: Ka-Band, Direct to Earth, MAVEN-class data rates.
Features
Localization and diurnal concentrations of methane and water and its isotopologues.
Science Objective
4D SCIENCE
Constellation
Notes: (Telecom of up to MAVEN-class relay could be included, but it is not in the baseline.)

## Slide 28
How to do it small?
What mission concepts?
What science?
Why Mars?
Last thoughts & summary

## Slide 29: Summary Thoughts & Discussion
Several emerging trends are creating a unique new opportunity for compelling Mars science missions at radically reduced cost relative to Discovery
  Low-cost rideshare and new commercial launch vehicle providers
  Efficient smallsat-scale EP solutions for Mars transfer from GTO
  New small-mass instruments that can achieve decadal-class science.
  Low-complexity hard-lander concepts for Mars surface access
  $100M - $300M represents a technological “sweet spot” with high science return above current SIMPLEx $55M cap.
Opportunities?
  Refine focused Mars science mission concepts suited to smallsat implementation
  Consider smallsat missions for critical Mars infrastructure (e.g., telecom relay, hi-res recon…)
  Seek international partnerships leveraging complementary capabilities to further affordability.
  Going together massively reduces the cost/unit.
Total Mission Cost
0
$200M
$400M
$600M
$800M
$1B
SIMPLEx
$55M
$500M + ELV
Discovery
$850M + ELV
New Frontiers
New Smallsat Class?

## Slide 30: Why particularly Mars for SmallSats?
Mars is especially well suited for a SmallSat Opportunity because:
Close enough to keep costs low enough to enable SmallSats to perform decadal-class science.
Hotspot for international collaboration (in the early 20ies missions lifting off from China, the Emirates, ESA, JAXA, and India; plans growing in Australia, Canada and Poland as well)
Commercial capabilities will enable soon to explore Mars: Mars as a testbed and catalyzer for commercial contributions to the exploration of Venus, asteroids and beyond.
BUT ALSO: Mars Exploration support from the Artemis program and growing HEO support for Mars Program in SMD.

## Slide 31: Mars SmallSats in the 2020ties can…
Ⓒ National Geographic, 1967.
Ⓒ 20th Century Fox’s “The Martian”