## Slide 1
HAWK
The deep space platform for navigation, communication, and scientific exploration
S. Simonetti
Copyright © Argotec S.r.l. 2021. All right reserved.

## Slide 2: HAWK – The Deep Space Platform
Outline
Argotec Company Overview
HAWK Platform Overview
On-going Missions
  ArgoMoon
  LICIACube
  MARS COMM NAV
  ANDROMEDA
Next Targets

## Slide 3: ARGOTEC Company Overview

## Slide 4: ARGOTEC Company Overview
Location
Turin (Italy)
Largo, MD (USA)
Cologne (Germany)
Noordwijk (Netherlands)
Argotec US subsidiary allows to work in close proximity to the key space players and customers (e.g. NASA)
Branches in Germany (EAC) and Netherlands (ESTEC) allow the company to support also ESA strategic activities

## Slide 5: HAWK Platform Overview

## Slide 6: HAWK Platform Overview
Main Features
300krad Deep Space Rad-Hard Avionics
HI-REL EEE components with flight heritage
SADA
Up to 8/9 U of Payload bay
Fully compatible with various ground segment DSN connection
Autonomous Target Tracking & Navigation
Autonomous Attitude Recovery
Autonomous FDIR
100 Mbps max Data Rate
5 + years Lifetime
Avionics processing capabilities able to support Artificial Intelligence
RAD-HARD & RELIABLE
AUTONOMOUS
PERFOMANT
MISSION-ADAPTABLE

## Slide 7: HAWK Platform Overview
Performance
6U
27U
12U
 | 6 U | 12U | 27U
PAYLOAD MASS | up to 3 kg* | up to 12 kg* | up to 30 kg*
PAYLOAD VOLUME | up to 3.5U* | up to 8U* | up to 15U*
PAYLOAD PEAK POWER | up to 40W | up to 40W | up to 80W
POWER SYSTEM | 3.3V, 5V, 12V, 28V Secondary battery up to 120Wh | 3.3V, 5V, 12V, 28V Secondary battery up to 250Wh | 3.3V, 5V, 12V, 28V Secondary battery up to 480 Wh
SOLAR ARRAY PEAK POWER | 40W, or 80W | 40W, 80W, or 120W | up to 300W
SINGLE AXIS SUN TRACKING SOLAR ARRAY DRIVE | Yes | Yes | Yes
ATTITUDE DETERMINATION | Sun sensors, Star Tracker, Accelerometers | Sun sensors, Star Tracker, Accelerometers | Sun sensors, Star Tracker, Accelerometers
GUIDANCE, NAVIGATION AND CONTROL | Delta DOR, sequential ranging, pseudonoise ranging, GNSS** | Delta DOR, sequential ranging, pseudonoise ranging, GNSS** | Delta DOR, sequential ranging, pseudonoise ranging, GNSS**
POSITION KNOWLEDGE | +/- 5m | +/- 5m | +/- 5m
DATA BUSES | RS422, LVDS, SpaceWire, SPI, I2C, CAN** | RS422, LVDS, SpaceWire, SPI, I2C, CAN** | RS422, LVDS, SpaceWire, SPI, I2C, CAN**
BUS PROVIDED DATA STORAGE | up to 32 GB | up to 32 GB | up to 64 GB***
COMM | Uplink: UHF, S-Band, X-Band, K-Band** | Uplink: UHF, S-Band, X-Band, K-Band** | Uplink: UHF, S-Band, X-Band, K-Band**
 | Downlink: UHF, S-Band, X-Band, K-Band** | Downlink: UHF, S-Band, X-Band, K-Band** | Downlink: UHF, S-Band, X-Band, K-Band**
COMMAND AND TELEMETRY RADIO TRANSMITTERS | 1kbps to 100Mbps | 1kbps to 100Mbps | 1kbps to 100Mbps
COMMAND AND TELEMETRY RADIO RECEIVERS | 100bps to 30Mbps | 100bps to 30Mbps | 100bps to 30Mbps
PROPULSION | up to 70 m/s (chemical propulsion) up to 600 m/s (electrical propulsion) | up to 160 m/s (chemical propulsion) up to 1 km/s (electrical propulsion) | up to 400 m/s (chemical propulsion) up to 3.5 km/s (electrical propulsion)

## Slide 8: On-going Missions

## Slide 9: On-going Missions
ArgoMoon Mission Overview
2021
ArgoMoon
Artemis-1 mission (NASA)
Planetary Observation
Mass: 14 kg
Dimensions: 6U (34x20x10 cm)
Orbit: High Elliptical Orbit
Launch Vehicle: NASA
Sponsor: Italian Space Agency
Launch date: 2021
Features: Autonomous Tracking, High speed data relay, AI, Rad-hard technology
Inserire foto AGM

## Slide 10: On-going Missions
ArgoMoon Mission Timeline
T0 : DEPLOYMENT
Closure of the separation switches: power to the system
T0 + 1 MIN
ICPS Targeted:
Tracking Mode
ATTITUDE reconstruction
T0 + 15 SEC
Pointing Cameras towards ICPS
T0 + 5 MIN
PS operational:
Relative dynamic maneuvers
100m-500m proximity flight
1st picture
T0 + 8 HR
Geocentric orbit
Pictures of Earth and the Moon and validation of on-board Technologies
ORION DETACHMENT FROM ICPS
Put in a Translunar Trajectory
T0 + 5.5 MONTHS
Enter in heliocentric orbit for the disposal phase

## Slide 11: On-going Missions
ArgoMoon Autonomous Navigation

## Slide 12: On-going Missions
LICIACube Mission Overview
2021
LICIACube
DART mission (NASA)
Planetary Defense
Mass: 14 kg
Dimensions: 6U (34x20x10 cm)
Orbit: Heliocentric Orbit
Launch Vehicle: NASA
Sponsor: Italian Space Agency
Launch date: 2021
Features: 2 Cameras, Fast Fly-by Maneuvering, Long Cruise Autonomous Re-activation, Autonomous Nav, Track & Pointing
Inserire foto LCC

## Slide 13: On-going Missions
LICIACube Mission Timeline
PIGGYBACK CRUISE PHASE
LICIACube is carried by DART S/C
SCIENCE
LICIACube performs separation maneuvers and acquires pictures of Didymos B and plume generated by the DART S/C impact
LICIACUBE DEPLOYMENT
DART S/C trigger the LICIACube deployment 120 hours before the impact
APPROACHING PHASE
LICIACube establishes a link W/DSN to perform the satellite tracking and the orbit determination
SCIENCE
Downlink of acquired scientific data for 6 months
LAUNCH
Launch Window June-July 2021

## Slide 14: On-going Missions
LICIACube Autonomous Navigation
Nominal
Trajectory
Asteroid Tracking Control Loop
Attitude Control Loop
Attitude Determination and Control System
Objects Detection
Trajectory Recognition
Autonomous asteroid tracking
Multi-subsystem interaction
Robust to spatial and temporal uncertainties

## Slide 15: On-going Missions
ANDROMEDA Concept
Mission Control Center
Service Control Center
Ground
Stations
Lunar
Users
Satellite
Constellation
Earth
Users

## Slide 16: On-going Missions
ANDROMEDA Mission Features
ANDROMEDA is an innovative microsatellite constellation for communications in lunar environment to establish a service based on:
High speed communication system implementation
Small satellite platform architecture use
Multi-users service provision
Real time telecommunication network creation
24/7 Lunar South Pole coverage
Full Lunar coverage

## Slide 17: On-going Missions
MARS COMM NAV Mission Features
MARS COMM NAV is an innovative microsatellite constellation for communications and navigation in mars environment to establish a service based on:
High speed communication system implementation
Small satellite platform architecture use
Multi-users service provision
Real time telecommunication network creation
24/7 Global coverage of Mars

## Slide 18: Next Targets

## Slide 19: Next Targets
Possibile Application of HAWK Platform

## Slide 20
THANK YOU!
www.argotecgroup.com
Copyright © Argotec S.r.l. 2021. All right reserved.