## Slide 1: CATSAT: A 6U Inflatable antenna technology demonstrator mission Aman Chandra1, Christopher K. Walker1,2, Juan Carlos Tonazzi2 1 Aerospace and Mechanical Engineering, The University of Arizona 2 FreeFall Aerospace, Inc

## Slide 2
Introduction
Antenna Technology | Surface Area (m2) | Mass (kg) | Stowed Volume (m3) | Packing efficiency | Mechanical Complexity | Scalability
Fixed reflectors | 1.2 | 2 - 5 | 0.8 | 1:1 | None | Poor
Mechanically deployable reflectors | 1.2 | 2.1 | 0.04 | 5:1 | High | Poor
Foldable reflect-arrays | 1.1 | 0.6 – 0.8 | 0.05 | 3:1 | Low | Moderate
Inflatable reflectors | 1.2 | 0.2 - 0.3 | 0.02 | 20:1 | Low | High
Table: HGA technology comparison*
High gain antenna (HGA) technology for CubeSats:

## Slide 3
Challenges
Design:
Multi-scale, multi-disciplinary problem.
Inadequate numerical simulation tools.
Scaling laws not well understood.
Manufacture:
Complex and high-cost manufacturing processes.
Limited availability of high-performance materials.
Flight operations:
Risk of micrometeoroid damage.
Thermal gradients effect on membrane shape.
Degradation of membrane on orbit.
Un-characterized vibration modes
Figure: Inflatable antenna experiment on board STS 77

## Slide 4: Related development
Inflatable antenna technology for CubeSats:
  Work has been underway to enhance reliability
  Technologies demonstrated in laboratory environments include
    Passively controlled inflation mechanisms - Babuscia., et al. (2014, 2015).
    Inflatable membrane rigidization - Babuscia., et al. (2016, 2017).
    CubeSat packaging and deployment systems - Chandra., et al.(2019).
    Actively controlled inflation systems - Chandra., et al. (2020).
  On-orbit demonstration needed to fully understand extent of reliability.

## Slide 5
Tests performed on a NASA high altitude balloon flight funded by the Office of Naval Research (ONR).
Long time-scales in microgravity and vacuum needed to evaluate structural and communication performance of inflatable antenna.
LEO exposure will evaluate effect of micro-meteorites, oxygen corrosion, UV exposure, temperature cycling.
It works!
High altitude test
View at 30 miles altitude
“Big 60”: Aug. 2018

## Slide 6: Mission Description
6U CubeSat technology demonstrator mission
  Selected for launch under NASA CSLI program.
  Sun synchronous orbit at 550 km.
  Launch NET April 2022 on board Fire-Fly Black Alpha.
  Nominal mission lifetime: 6 months.
Payload
  Inflatable antenna deployment system.
  Instrument module.
  WSPR antenna deployment system.
  Metrology module.

## Slide 7: Mission Requirements
Primary Mission Objectives:
  High bandwidth transmission link demonstration from a 0.5 m diameter inflatable antenna system.
  Ionospheric measurements: WSPR implements a protocol designed for probing potential propagation paths between amateur radio stations utilizing low-power transmissions.
Secondary Mission Objectives:
  Metrological study of inflatable membrane surface

## Slide 8: System Overview
X-Band
Up/Down Converter
Power
Splitter
X-Band Patch
Antenna
AstroSDR
UHF Radio
HF/VHF
Upconverter
HDMI Camera
Solar
Panels
PCS
Deployment
System
UHF Antenna
HF Antenna
X-Band Antenna
10.5 GHz
~50 Mbps
46 cm Whip
Duplexer
TRAK C800124/DK
ADCS
Std. Camera
HD Images
Antenna Images
Ethernet
RX1 TX1
RX0
Computer
Spacecraft Bus
435-438 MHz
5-30 MHz
130-155 MHz
3.5 GHz
Spherical Reflector
10.5 GHz
Pwr Amp
LNA
Qorvo
TGC2510/2610
TGA2511
TGA2700
CAN
UART
I2C
GPIO (3 pins)

## Slide 9: System Overview
Feed support structure
Vectran ties
Line feed unit
Deployable solar panel
Antenna metrology module
Battery pack
Avionics stack
AD&CS
Whip antenna deployer
HD camera
ASTRO SDR
Microwave upconverter
GPS antenna
X-band patch antenna
Radiator panel
WSPR antenna
UHF antenna

## Slide 10: Concept of operation

## Slide 11: Science traceability matrix
Science/Technology Questions | Objective | Measurement Requirement | Mission Requirement
How can high telecom bandwidths be achieved with a CubeSat? | Demonstrate a deployable, high gain antenna | Relay high- definition images from orbit in near real time | Orbital platform HD Camera imaging system Inflatable, 0.5m reflector X band data link ~550 km, sun synchronous orbit >1 month
How does the structure of the ionosphere vary from day to night? | Measure ionospheric structure along the terminator | Monitor multiple HF WSPR beacons above the ionosphere | Orbit along terminator >500 km altitude >1 month

## Slide 12: 1.5 U Packaging and deployment system
150 mm
90 mm
80 mm
500 mm

## Slide 13: Inflation gas delivery and control system
95/5 Argon – Helium mixture for chosen for inflation.
Gas release and control system has been built and tested.
The intent is to over-pressurize the inflatable to compensate for relative loss in pressure during eclipse phases.

## Slide 14: Line feed system – spherical correction
Line feed within the 0.5m reflector
Bare line feed for the HGA
Spherical reflector antenna

## Slide 15: Line feed sensitivity
The gain from just the antenna is 26.7 dBi and the first side-lobe level is -18 dB.
A peak directivity of 31 dBi is expected assuming no losses.
Figure 10 shows the LHCP component of the antenna pattern and shows it is primarily left-hand circular polarized.
On-going and future work

## Slide 16: Line feed sensitivity
The return loss of the feed shows it is optimized to be resonant at 10.5 GHz and impedance-matched with a 50ohm source.
The HGA is optimized for communications between the 6.1 m ground stations and the spacecraft.
The HGA will primarily be used to downlink image data taken by the spacecraft’s on-board cameras and serve as a technology demonstrator.
On-going and future work

## Slide 17: Line feed sensitivity – Antenna gain

## Slide 18: Line feed sensitivity – Return Loss

## Slide 19: Instrument Module
HD camera
Camera control boards
HF Upconverter
ASTRO SDR
Stowed WSPR antenna
Burn Wire release
560 mm
110 mm
90 mm
80 mm

## Slide 20: WSPR Antenna Deployment

## Slide 21
AstroSDR
Dual receivers & transmitters, 70 MHz to 6 GHz
Xilinx Zynq Z-7045 FPGA
Embedded Linux OS for reliable operation
64 GB eMMC flash
WSPR Downlink Channel Format

## Slide 22: Current Status
On-going work:
Inflatable antenna system undergoing TVAC testing.
Pre-flight prototype hardware realized and undergoing testing.
Planned work:
Near-field measurements from reflector using line feed.
Measurement of S11 return loss.
Integration and testing with spacecraft bus.

## Slide 23: References
A. Babuscia, T. Choi, and K.-M. Cheung, “Inflatable antenna for CubeSat: Extension of the previously developed S-Band design to the X-Band,” presented at the AIAA SPACE 2015 Conference and Exposition, Pasadena, California, Aug. 2015, doi: 10.2514/6.2015-4654.
A. Babuscia, J. Sauder, A. Chandra, J. Thangavelautham, L. Feruglio, and N. Bienert, “Inflatable antenna for CubeSat: A new spherical design for increased X-band gain,” in 2017 IEEE Aerospace Conference, Mar. 2017, pp. 1–10, doi: 10.1109/AERO.2017.7943897.
A. Babuscia, T. Choi, J. Sauder, A. Chandra, and J. Thangavelautham, “Inflatable antenna for CubeSats: Development of the X-band prototype,” in 2016 IEEE Aerospace Conference, Mar. 2016, pp. 1–11, doi: 10.1109/AERO.2016.7500679.
A. Chandra, J. C. Lopez Tonazzi, D. Stetson, T. Pat, and C. K. Walker, “Inflatable membrane antennas for small satellites,” in 2020 IEEE Aerospace Conference, Big Sky, MT, USA, Mar. 2020, pp. 1–8, doi: 10.1109/AERO47225.2020.9172737.
Chandra, J. C. Lopez Tonazzi, D. Stetson, T. Pat, and C. K. Walker, “Development of inflatable spherical reflector antenna for X-band operation,” in 2020 IEEE Aerospace Conference, Big Sky, MT, USA, Mar. 2021