## Slide 1
Jet Propulsion Laboratory
California Institute of Technology
Highly Accurate Surface Propagation for Mars Helicopter mission
Telecommunication
Nacer Chahat, Fellow of IEEE
Gaurangi Gupta, Matthew D. Chase, and Courtney Duncan
NASA Jet Propulsion Laboratory / California Institute of Technology
© 2023 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2
Jet Propulsion Laboratory
California Institute of Technology
Team: D. Gonzalez, N. Chahat, G. Chattopadhyay
FEW THINGS TO KNOW
Notes: Rover telecom scenario

## Slide 3
Jet Propulsion Laboratory
California Institute of Technology
Team: D. Gonzalez, N. Chahat, G. Chattopadhyay
Helicopter antenna on its solar panel
425 mm
165mm
FM Helicopter antenna
Antenna design
(No blades)
θh
θh
Fasteners
(PEEK)
Radiating element (stainless steel)
PCB
(Arlon 85N)
Washers
(PEEK)
HELICOPTER
ANTENNA
Notes: Rover telecom scenario

## Slide 4
Jet Propulsion Laboratory
California Institute of Technology
Antenna design
Antenna
Antenna on M2020 Rover
Antenna testing on M2020 Rover mockup
FM Antenna
ROVER
ANTENNA
Helicopter Base Station Antenna (HBA) radiation pattern

## Slide 5
Jet Propulsion Laboratory
California Institute of Technology
Team: D. Gonzalez, N. Chahat, G. Chattopadhyay
LINK BUDGET CALCULATION
Propagation Link while the helicopter is on the ground:
Map coverage assuming min, mean, max polarization loss with blade rotating.
Rover
x
z
θh
Azimuth angle θh = [0°-359°]
Link geometry
Received power of >-99dBm  250kbps
Received power of [-108, -99] dBm  20kbps
No link

## Slide 6
Jet Propulsion Laboratory
California Institute of Technology
Team: D. Gonzalez, N. Chahat, G. Chattopadhyay
LINK BUDGET CALCULATION
Propagation Link while the helicopter is flying:
Map coverage assuming min, mean, max polarization loss with blade rotating.
Rover
x
z
θh
Azimuth angle θh = [0°-359°]
Link geometry
Received power of >-99dBm  250kbps
Received power of [-108, -99] dBm  20kbps
No link

## Slide 7
Jet Propulsion Laboratory
California Institute of Technology
Team: D. Gonzalez, N. Chahat, G. Chattopadhyay
FIELD TEST FOR VALIDATION
Lc=5.5dB
Pout=28.65dBm
Pmeas
ROVER
HELI

## Slide 8
Jet Propulsion Laboratory
California Institute of Technology
Team: D. Gonzalez, N. Chahat, G. Chattopadhyay
WHAT ABOUT ON MARS?
First Flight performed at 63m:
z
0
3m
Time (s)
PRx_calc = -51.0Bm
PRx_meas = -49.0±1dBm
PRx_calc = -39.7dBm
PRx_meas = -37±1dBm
PRx_calc = -48.6dBm
PRx_meas = -48.5±0.5dBm
N. Chahat et al., “The Mars Helicopter Telecommunication Link: Antennas, Propagation, and Link Analysis,” IEEE Antenna Propag. Magazine, vol. 62, no. 6, pp. 12-22, Dec. 2020.

## Slide 9
Jet Propulsion Laboratory
California Institute of Technology
WHAT ABOUT ON MARS?
Results for first 5 flight using methodology presented in [1]
[1] N. Chahat et al., “The Mars Helicopter Telecommunication Link: Antennas, Propagation, and Link Analysis,” IEEE Antenna Propag. Magazine, vol. 62, no. 6, pp. 12-22, Dec. 2020.
Accurate predictions for all 5 cases as they meet the criteria of applicability:
Distance between Tx and Rx >> antenna height
Surface is fairly flat
LOS is satisfied
Flight # |  | Altitude (m) | Distance (m) | Rover Yaw (degree) | Meas. Power (dBm) | Calc . Power (dBm) | Error (dB)
1 | Take Off | 0 | 63 | 175 | -49 | -51 | 2
 | In flight | 3 | 63 | 175 | -37 | -39.7 | 2.7
 | Touch down | 0 | 63 | 175 | -48.5 | -48.6 | 0.1
2 | Take Off | 0 | 63 | 175 | -48 | -48.6 | 0.6
 | In flight | 5 | 65 | 175 | -40 | -40.1 | 0.1
 | Touch down | 0 | 63 | 175 | -49 | -48.6 | 0.4
3 | Take Off | 0 | 63 | 175 | -49 | -46.6 | 2.4
 | In flight | 5 | 84 | 175 | -44 | -44.5 | 0.5
 | Touch down | 0 | 64 | 175 | -49 | -46.9 | 2.1
4 | Take off | 0 | 67 | 162 | -57 | -57 | 0
5 | Take off | 0 | 99 | 156 | -58 | -56.6 | 1.4
 | Touchdown | 0 | 112 | 156 | -66 | -64.2 | 1.8

## Slide 10
Jet Propulsion Laboratory
California Institute of Technology
Sol 178 (Communication Issues):
Distance of 372m
First Communication Discrepancy
Sol 178 - PE
Rover
Heli
PRx_meas = -97±1dBm
PJPL_Model = -75.5dBm
PDTRM = -87.9dBm
PDPM = -87.0dBm (updated path loss for low transmitter)
PPE = -96.3dBm
JPL model is no longer applicable in adverse topology.
Winprop was capable of predicting the marginal link.
Rx power distribution as a function of distance and elevation
Sol 178 | X | Y
Heli location | -707.8 | -654.5
Sol 178 | X | Y | Yaw
Rover location | -818.1 | -369.6 | -142.2

## Slide 11
Jet Propulsion Laboratory
California Institute of Technology
Sol 287 (Communication Issues):
Distance of 358m
Sol 287 - PE
PRx_meas = -96.2±1dBm
PJPL_Model = -81.1dBm
PDTRM = -99.6dBm
PDPM = -97.4dBm (updated path loss for low transmitter)
PPE = -96.7dBm
Heli
Rover
Winprop was capable of predicting the marginal link.
JPL model is no longer applicable in adverse topology.
Sol 287 | X | Y
Heli location | -686.1 | -177.9
Sol 287 | X | Y | Yaw
Rover location | -709.3 | -534.8 | -129.0
Rx power distribution as a function of distance and elevation
Second Communication Discrepancy

## Slide 12
Jet Propulsion Laboratory
California Institute of Technology
Flight 17:
Take off distance of 318m
Landing distance of 321m
Distance flown of 187m at a speed of 2.5m/s
First Communication Issue
Liftoff - PE
Touchdown - PE
Rover
Heli Liftoff
Heli Touchdown
Flight #17 | X | Y
Pt A (liftoff) | -859.3 | -249.3
Pt B (touchdown) | -686.1 | -177.9
Flight #17 | X | Y | Yaw
Rover location | -663.0 | -498.2 | -120.4
PRx_meas = -89±1dBm
PDTRM = -64.8 dBm
PDPM = -78.0 dBm
PPE = -84.8 dBm
PRx_meas = -103dBm
PDTRM = -78.5 dBm
PDPM = -78.4 dBm
PPE = - 108.4 dBm

## Slide 13
Jet Propulsion Laboratory
California Institute of Technology
Improved Telecom Analysis for Non Line of Sight Communication For Accurate Flight Planning was fully infused into the Ops tool
This tool shows the route for the Rover and the potential landing sites
For each landing site, the predicted received power generated using Altair Winprop is shown for three threshold
Operation Tool used for Flight Planning

## Slide 14
Jet Propulsion Laboratory
California Institute of Technology
We continue improving the predicts as we accumulate more statistics
We have now completed 51 flights and are currently in the most challenging location for telecom.
The error standard deviation remains under 3.1dB after 51 flights.
Operation Tool used for Flight Planning

## Slide 15
Jet Propulsion Laboratory
California Institute of Technology
Highly Accurate Surface Propagation for Mars Helicopter mission
Telecommunication
Nacer Chahat, Fellow of IEEE
Gaurangi Gupta, Matthew D. Chase, and Courtney Duncan
NASA Jet Propulsion Laboratory / California Institute of Technology
© 2023 California Institute of Technology. Government sponsorship acknowledged.