## Slide 1
First In-Flight Demonstration of Pseudo-Noise Delta-Differential One-Way Ranging
Chris Volk, Zaid Towfic, Mazen Shihabi, James Border

## Slide 2: Delta Differential One-Way Ranging (DDOR)
DDOR uses interferometry to measure spacecraft angular position in the radio reference frame
Observations from 2 (long) baselines are needed to measure both components of angular position

## Slide 3: DDOR Navigational Purpose
Complements line-of-sight Doppler and range to provide plane-of-sky coordinate targeting for critical events
  E.g. High accuracy is needed for targeting a Mars landing
  300 m plane-of-sky position accuracy at Mars (~1 AU)
Doppler, only
Doppler, Range
Doppler, Range,
& DDOR

## Slide 4: DDOR Advantages for Small Sats
Spacecraft only needs to transmit for a short time
  1 hour DDOR pass requires 40 min of spacecraft transmission
  30 min DDOR pass requires 10 min of spacecraft transmission
  DDOR is downlink only, so no need to sweep / acquire uplink
Can reduce antenna contention
  Observe multiple spacecraft within 1 DDOR pass
    E.g. Quasar – Spacecraft 1 – Spacecraft 2 – Quasar
  Replace lengthy ranging/doppler nav passes with short DDOR passes
    ~3+ hours of ranging/doppler vs 1 hour DDOR
  Important for crowded launches – e.g. Artemis 1 launch

## Slide 5: Current X-Band DDOR Error Budget
1 nanoradian
0.1 mas
100m @ 1AU
RSS Total
Leading Error Term

## Slide 6: Dispersive Phase, The Dominant Error
Dispersive phase is the difference between the instrumental phase shift of the spacecraft and quasar signals.
  Typical Dispersion error measured with strong quasar is 0.2°
Spacecraft = 0.2°
Quasar = 0.0°
Error = 0.2°

## Slide 7: Pseudo-Noise (PN) DOR Signal
The S/C signal is spread by a PN sequence.
  The resulting spectrum is spread by chip rate of the PN code, and flattened by use of a pulse shaping filter.
  Estimated cancellation of ~90% of the dispersion error.
  A long sequence (~1 ms) can be used for ambiguity resolution.
  CDMA techniques can measure multiple s/c simultaneously.
Sinusoidal DOR Signal
8 MHz PN-DOR Signal
8 Mcps PN Sequence
(quasar-like signal)

## Slide 8: Iris CubeSat Radio
The Iris radio has now flown on several space missions: MarCO-A/B, Lunar Flashlight, CAPSTONE etc.
26W consumption, 5W output, 0.5 U volume and 1.2kg
UHF / S / X / Ka-Band options available
DDOR successfully used on MarCO-A/B, LFL CubeSats
https://www.nasa.gov/sites/default/files/atoms/files/brochure_irisv2_201507.pdf
SSPA
LNA
Full Stack

## Slide 9: Iris CubeSat Radio PN DDOR Spectrum
Carrier Signal
PN DOR Signal ±19 MHz

## Slide 10: Iris PN DDOR Observations on LFL
Lunar Flashlight (LFL) 1st PN DDOR demo on Jan-7th
Improved ambiguity resolution of PN DOR proved useful

## Slide 11: Summary
DDOR provides critical navigation data with less spacecraft transmission than ranging/doppler and less antenna contention on busy launches
PN DDOR enhances Classic DDOR with improved ambiguity resolution and performance
The Iris radio has successfully demonstrated PN DDOR in-flight on Lunar Flashlight