## Slide 1: Evaluation of Tensegrity Telescopes for Small Satellites on Asteroid Recon Missions

## Slide 2: High Level Overview
Mission:
“To design, develop, manufacture, and test a small spacecraft formfactor 2 mirror deployable tensegrity telescope for Near Earth Asteroid detection (NEA).”
System Capabilities
  Detecting NEA's 100m in size with albedos between 0.05 and 0.1
  Weigh no more than 8kg
  Stowed volume shall not exceed 8000cm^3
System Design
  12U CubeSat
  Cassegrain Telescope design with HyperStar from Starizona

## Slide 3: High Level Overview

## Slide 4: Optical System
Originally planned to replicate SCT optical design with our structural design
Plan is to disassemble COTS SCT, & rebuild with its components around deployable structure
Due to volume restriction of CubeSat & optical geometry of SCT design, needed to adjust plan
Turned to local telescope store, Starizona, for advice and potential future sponsorship
HyperStar, built by Starizona, provided a perfect solution.
  Replaces secondary mirror at top of SCT
  Provides simple method to attach camera above structure
  f/2 focal ratio provides very small exposure time for a very quick and easy imaging
Original 6" SCT Optical Design w/ Camera Behind Primary Mirror
6" SCT Optical Design w/ HyperStar/Camera Assembly
*Above Diagrams provided by Scott Tucker at Starizona

## Slide 5: Optical System, Cont.
Comprised of three components:
  Celestron C6-A OTA (6" SCT)
  HyperStar 6 v4 (Multi-Lens Corrector) by Starizona
  ZWO ASI174MM Monochrome Imaging Camera
OTA will be disassembled into components:
  Primary mirror & corrector plate with threading for HyperStar will be used with our deployable structure
Prototype for design day will be tested at night time in the local Tucson desert
  Goal is to have images showing optical system capabilities, as well as deployment and control of telescope structure
https://www.youtube.com/watch?v=O9RYy27Ppb0

## Slide 6: Optical System, Cont.
Optical System Specifications:
  HyperStar/OTA:
    ~150mm aperture
    ~300mm focal length
    f/2 focal ratio
    Will detect NEA's of abs magnitude of 10.7
  Camera:
    1936 x 1216 resolution (2.4 MP)
    CMOS Sensor
    12-bit ADC
    Monochrome Camera
    164 FPS
https://www.youtube.com/watch?v=O9RYy27Ppb0

## Slide 7: High Level Overview
Internal structure and major subsystems
Primary mirror and rods
Corrector plate and HyperStar
Entire assembly
Bottom case with servos and primary mirror

## Slide 8: Con Ops
Structure Deployment
Measure distances and verify level platform
Make Adjustments as needed
Point at spot in space.
Take multiple exposures and downlink images
Compare objects with known objects database

## Slide 9: Test Plans

## Slide 10: Test Results – Optical

## Slide 11: Test Results – Optical cont.

## Slide 12: Mechanical Prototyping

## Slide 13: Mechanical Prototyping

## Slide 14: Complete Prototype
TBD

## Slide 15: Conclusion
TBD