## Slide 1: Evaluation of Tensegrity Telescopes for Small Satellites on Asteroid Recon Missions
Hilliard Paige III (Presenting)
Jared Pavek
Javier Alday
Quinn Lamey
Matthew Walton

## Slide 2: Problem Statement
Detection of near-earth asteroids (NEA) has become increasingly important for scientific and planetary defense applications
  Thousands of NEA’s have yet to be cataloged or tracked
Most NEA detection is conducted with ground-based telescopes
  Space-based platforms are cost prohibitive
  Ground stations are plagued by light pollution, atmospheric disturbance and space debris.
This work aims to fill this capability gap in NEA detection
  Smallsats allow for low-cost dedicated space-borne platforms.
Notes: Pretty picture of asteroid

## Slide 3: High Level Overview
Mission:
To design, develop, manufacture, and test a prototype small spacecraft formfactor 2 mirror deployable tensegrity inspired telescope for Near Earth Asteroid detection (NEA).
System Capabilities
  Detecting NEA's 100m in size with albedos between 0.05 and 0.1
  Weigh no more than 8kg
  Stowed volume shall not exceed 8000cm^3
System Design
  12U CubeSat
  Cassegrain Telescope design with HyperStar from Starizona
Constraints (senior design project)
  Budget: $3000
  Timeline: 6 months
  Personnel: Undergraduate Students only
Notes: Replace with actual design

## Slide 4: Con Ops
UHF ground station
X-band downlink station
Launch
SC Deployment
Deploy solar panels and UHF comms
Credit: Exolaunch
Telescope deployment and checkouts
Begin exposures of points in space,
Downlink
Credit: ISISSpace
Credit: Firefly Aerospace

## Slide 5: Optical System
Original 6" SCT Optical Design w/ Camera Behind Primary Mirror
6" SCT Optical Design w/ HyperStar/Camera Assembly
Modified SCT design using corrector lens (HyperStar)
Notes: Originally planned to replicate SCT optical design with our structural design
Plan is to disassemble COTS SCT, & rebuild with its components around deployable structure
Due to volume restriction of CubeSat & optical geometry of SCT design, needed to adjust plan
Turned to local telescope store, Starizona, for advice and potential future sponsorship
HyperStar, built by Starizona, provided a perfect solution.
  Replaces secondary mirror at top of SCT
  Provides simple method to attach camera above structure
  f/2 focal ratio provides very small exposure time for a very quick and easy imaging

## Slide 6: Optical System, Cont.
Comprised of three components:
  Celestron C6-A OTA (6" SCT)
  HyperStar 6 v4 (Multi-Lens Corrector) by Starizona
  ZWO ASI174MM Monochrome Imaging Camera
OTA will be disassembled into components:
Optical Specifications
  HyperStar/OTA:
    ~150mm aperture
    ~300mm focal length
    f/2 focal ratio
    Will detect NEA's of abs magnitude of 10.7
  Camera:
    1936 x 1216 resolution (2.4 MP)
    CMOS Sensor
    12-bit ADC
    Monochrome Camera
    164 FPS
https://www.youtube.com/watch?v=O9RYy27Ppb0

## Slide 7: High Level Overview
Exploded View
Deployment Demo
Notes: Talking more about how everything integrates.
Key features of the system (the deployment)
-Deployment CAD

## Slide 8: Mechanical Prototyping
Prototypes have been constructed out of wood and 3D printed materials to cut costs
Design went through 4 total iterations.

## Slide 9: Mechanical Prototyping cont.

## Slide 10: Test Results – Optical
First light testing with stock OTA
Data analysis and star solver using Astrometry

## Slide 11: 1-second exposure tests
Mars and surrounding stars
Ceres and surrounding stars
1-Second exposures yield detection of objects with magnitude 13. Further testing required.
Notes: 1 second unprocessed exposures. – According to plate solving software, detected down to between 12 and 13 have been confirmed.

## Slide 12: Complete Prototype
Tested Mechanical Deployment
Servos are not the final model due to time and budget constraints
Works extremely well
Mylar blankets surround the structure to reduce stray light when capturing images

## Slide 13: Conclusions and Future work
The team has successfully matured the design to Technology Readiness Level 4, proving both the mechanical deployment of the prototype and the optical properties
Further work is required to mature the prototype to fit into a CubeSat form factor
Source: NASA JPL
Notes: Selling points: cots components.
Designed the means of packaging a large telescope into a small form factor.

## Slide 14: QUESITONS?
Special thanks to:
Adrien Bouskela
Scott Tucker
Dr. Sergey Shkarayev
Dr. Jekans Thanga