## Slide 1
Strictly Confidential
1
Radioisotopic Propulsion for Small Satellites
Jeremiah Pate

## Slide 2: MPD thrusters are the only > TRL 5 technology that allows both high thrust and high specific impulse (>10N and >5,000 s) The primary technological barrier is the high input power, often exceeding 100 kW (Choueiri, 2009), incurred from multiple steps from power source to power conversion to plasma heating
MPD Thrusters
Source: NASA

## Slide 3: Nuclear electric propulsion has been proposed numerous times in concert with MPD technology Weakness lies in the multiple conversion steps required and associated loss of efficiency, as well as the kW/kg ratio of the reactor itself More recently the VASIMR engine was claimed to be capable of a 39-day Mars voyage, but this was based on an unprecedented 1 kg/kW reactor power density (Webber, 2011), compared to the 100 kg/kW that has been previously achieved on spacecraft (e.g., TOPAZ reactor)
MPD Thrusters: Nuclear Option
SNAPSHOT, the first satellite to use nuclear electric propulsion, launched in 1965 (Courtesy: Department of Energy)

## Slide 4: What if there was a way to directly convert nuclear power to hot plasma?
Alternative

## Slide 5
Radioisotope Ion Propulsion
Xe
Xe
Xe+
Xe+
Partially inspired by Forward (1995), who suggested alpha emitters on a plastic thin film would result in both thrust and electrical power, as well as the “fission sail” described by Moeckel (1977)
Direct conversion approach, where alpha particles ionize and heat neutral propellant

## Slide 6: Given plasma is quasineutral, eliminating the need for a neutralizing cathode (Andres, 2011) An 80% efficiency for the magnetic nozzle is assumed, which is reasonable based on Andres (2011) and Zheng (2021)
Thruster Design
Xe
Xe
Xe+
Xe+
A solenoidal magnetic nozzle configuration is used for focus the beam of plasma particles

## Slide 7
Radioisotope Considerations
An ideal fuel is Americium-241, given its availability and low cost
Sample of Americium from a smoke detector (Source: Andrew Magill)
Am-241 metallurgy and chemistry is well understood enough to create thin-film structures, with the ideal thickness near 10 microns as suggested by Forward (1994)
Optimal alpha emitter has a long enough half life to be constant over the course of the mission, but a high enough specific activity for plasma heating

## Slide 8: Time-of-flight based on constant thrust approximation with a tangential burn lasting full duration of spiral-out orbit (Curtis, 2013)
Simulation Assumptions and Parameters
Total thruster mass (excluding radioisotope fuel) including structure and magnetic windings estimated to be 1 kg
Mass of the satellite structure and payload chosen to follow CubeSat mass standards

## Slide 9
Chart: Thrust
| 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000
 | 2.2 | 3.1 | 3.9 | 4.4 | 5 | 5.5 | 5.9 | 6.3 | 6.7 | 7
Chart: Specific Impulse
| 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000
Ratio vs Isp Isp | 8164 | 5774 | 4713 | 4082 | 3651 | 3333 | 3086 | 2887 | 2721 | 2581
Performance Modulation through Xe: Variation

## Slide 10
Mission Parameters
Mission Target | Mars | Mars | Jupiter
Formfactor | 6U | 12U | 12U
Total Mass (kg) | 7.1 | 9.6 | 14
Propellant Mass (kg) | 1.1 | 1.6 | 5.9
Americium Mass (kg) | 1 | 3 | 3
Time of Flight (days) | 133 | 56 | 205
Total Delta-v (km/s) | 7.3 | 7.4 | 22

## Slide 11
Thruster Parameters
Mission Target | Mars | Mars | Jupiter
Xe:α Ratio | 3500:1 | 4000:1 | 4000:1
Specific Impulse (s) | 4400 | 4100 | 4100
Thrust (mN) | 4.2 | 13 | 13
Specific Thrust (N/kW)* | .04 | .04 | .04
Plasma Temperature (eV)** | 47 | 42 | 42
Exhaust Velocity (km/s) | 43 | 40 | 40
Total Delta-v (km/s) | 7.3 | 7.4 | 22
*For reference, VASIMR and Hall effect thrusters have a specific thrust of .02 N/kW and .07 N/kW, respectively (Andres, 2011)
** 1eV = 11,605 K

## Slide 12
Future Work
Particle-in-cell simulations needed to optimize Xe:α ratio and structure of magnetic nozzle for a given plasma density
Analysis with other propellants such as Cesium, Iodine, Argon and Krypton
Regarding mission design, the calculations described assume constant thrust. A detailed mission design tool (i.e., Copernicus) could be used to include the impact of variable specific impulse on such a mission

## Slide 13: Sources
Andres, M. C. P., & Nikolai, T. (2011). The VASIMR engine: benefits, drawbacks, and technological challenges. IEPC2011-251.
Choueiri, E. Y. (2009). New dawn for electric rockets. Scientific American, 300(2), 58-65.
Curtis, H. (2013). Orbital mechanics for engineering students. Butterworth-Heinemann.
Forward, R. (1995, July). Radioisotope sails for deep space propulsion and electrical power. In 31st Joint Propulsion Conference and Exhibit (p. 2596).
Gilland, J., & Johnston, G. (2003, January). MPD thruster performance analytic models. In AIP Conference Proceedings (Vol. 654, No. 1, pp. 516-524). American Institute of Physics.
Ilin, A. V., Cassady, L. D., Glover, T. W., & Chang Diaz, F. R. (2011, March). VASIMR® human mission to Mars. In Space, Propulsion & Energy Sciences International Forum (pp. 1-12).
Moeckel, W. E. (1977). Thrust-sheet propulsion concept using fissionable elements. AIAA Journal, 15(4), 467-475.
Webber, C. R. (2011). Plasma, Ion-Thrusters, and VASIMR. ASEN, 5053, 1-9.
Zheng, J., Liu, H., Song, Y., Zhou, C., Li, Y., Li, M., ... & Zhao, B. (2021). Integrated study on the comprehensive magnetic-field configuration performance in the 150 kW superconducting magnetoplasmadynamic thruster. Scientific Reports, 11(1), 20706.