## Slide 1
Fast transit outer planet exploration with small satellites
Artur Davoyan

## Slide 2
9 missions
4 missions
1 mission
1 mission
1 mission
Deep Space Exploration Today
2 missions
60 years of space exploration
2 missions

## Slide 3
Challenges
Need to scale exploration
Travel takes many years (>7 years to Saturn)
Flagship missions are costly
Outer planet Exploration
Science Objectives
Search for life
Understanding planetary formation
Understanding solar system formation
Triton-Neptune system
“cursed cycle”
Not suitable for CubeSats
(reliability)

## Slide 4
Possible solution
Limited by the rocket equation
Reduce time of flight
Key challenge

## Slide 5
Image credit: the Planetary Society
Solar sails

## Slide 6
Solar Sails Flown and Planned
LightSail2 (2019)
Privately funded sail ($7M)
Image credit: The Planetary Society
Image credit: NASA
IKAROS (2011)
The first interplanetary sail
Image credit: JAXA
NEA Scout (2022)
The first science mission
315 kg
14m x 14m
4.5 kg
32 m2
10 kg
86 m2

## Slide 8
Trajectory & mission profile
C3=0
Start with MEO and “spiral out”
A.R. Davoyan et al., Optica 8, 722 (2021)
>20 AU/year for <0.2 AU perihelion with a lightweight spacecraft (A/m>50 m2/kg)

## Slide 9
Outstanding challenges
Harsh environment
Need for new materials
Large lightweight architectures
Spacecraft controls & navigation
Power and communications

## Slide 10
Credit: NASA
Current sail material technology
Limited to ~0.5 AU perihelion

## Slide 11
Solar power absorbed = Thermal power emitted
A. Davoyan et al., Optica 8, 722 (2021)
Solar radiation flux and thermal balance
Notes: Radiative heat transfer – only means

## Slide 12
7
Sail Materials for Small Perihelion Pass
metals
High temperature inorganic film
100nm
500nm-1000nm
Estimated density: <1.5 g/m2
Tested at ~500C (no degradation found)
Range of materials developed for small perihelion missions
Sail temperature <700 K at 0.1 AU perihelion

## Slide 13: SailCraft Architecture
NEA Scout example
6U cubesat
14 kg mass
85 m2 sail

## Slide 14: SailCraft Architecture
~15kg spacecraft bus
~2g/m2 sail material areal density
50-70g/m boom density
50m x 50m sail area
~25 kg total mass
12U – 16U CubeSat

## Slide 15
<10R☼
10-20 AU/yr
Fast Transit Outer Planets
Enabling Novel Breakthrough Missions
10-20 R
Probing inner solar corona

## Slide 16: SailCraft Architecture
Outer planet flyby probes
(needs development)
Heliophysics
(near term)
Iris radio
PV for power
1-2 instruments
Autonomy
Optical communications
RTGs for power (??)
1-2 instruments
Autonomy

## Slide 17
SCOPE
Quantum dot spectrometer for high throughput sensing
PI M. Sultana
Using sail as an instrument

## Slide 18
Vision: Sun as a Launch Pad
Oort cloud
Kuiper belt
Goals:
low cost (~$10M)
short lead time
missions to arbitrary destinations (e.g., high inclination)
fast (>20 AU/year)

## Slide 19
Pellet-Beam Propulsion for Breakthrough Space Exploration

## Slide 20: Team and Acknowledgements
Collaborators: S. Mahmooda, H. Helvajian, M. Velli, L. Johnson, S. Turyshev, D. Garber, L. Friedman, P. Hon, J. Carr, M. Nehls, M. Finckenor
UCLA student team: H.T. Tung, T. Joly-Jehenne, H. Jo, H. Ling, E. Haynes, P. Krings, J. Digani, S. Huang, A. Dunn, S. Martinez, R. Rio