## Slide 1: An Updated Parametric Design of a Torsion Pendulum to Demonstrate Attitude Control Using Microoptoelectromechanical System Control of Radiation Pressure
Jonathan Messer
Doctoral Student
jmesser@usc.edu
Joshua Pastizzo
Graduate Student
pastizzo@usc.edu

## Slide 2
Conserve Momentum Dumping Fuel by Controlling Solar Radiation Pressure

## Slide 3: The Problem
Environmental Torques act against Spacecraft continuously
Spacecraft attitude is maintained by storing angular momentum using Reaction Wheels or Control Moment Gyroscopes
Momentum Dumping is required to prevent material failure
  Magnetic Torquers are ineffective at or above GEO (especially for the pitch axis)
  Reaction Jets consume finite fuel
Fuel for Momentum Dumping becomes a Mission Lifetime Limitation
Solar Radiation Pressure is normally a perturbing force

## Slide 4: Existing Methods of Attitude Control using Solar Radiation Pressure
(Lievre, 1985)
(Sidi, 1997)
(T. Tsuda et al, 2011)
Lievre Method
IKAROS Method
Yaw
Roll

## Slide 5
Utilizing Digital Micromirrors Devices for Satellite Attitude Control

## Slide 6: Digital Micromirror Device (DMD)
An array of individually addressable pivoting mirrors
  Developed in 1987 by Texas Instruments, commercially available since 1992
  By 2002, over 1.5 million units sold
Each mirror is electrostatically commanded to a fixed tilt
The method of manufacturing is similar to semi-conductors
Emerging Applications
  3D Printing and Scanning
  Lithography
  Volumetric Displays
  Space-Based Astronomy
Printed with permission of Texas Instruments Inc.
786,432 micromirrors on this DMD
Micromirrors under Electron Scanning Microscope
A human blood cell is 6-8µm
Today’s Micromirrors are 5.4 µm

## Slide 7: Application of DMDs to Satellite Attitude Control
Rotation about XD
Rotation about YD
Force On/Off States for one square meter
On
Off
Center of Pressures Example Random Array
Torque Example Array Patterns and Varying Sun Angle
All On
Left On, Right Off
Top On, Bottom Off
Checkerboard
Max Cumulative Force per square meter
for varying sun angles
Notice that the COP location differs for each state
This method generates torque about all three axes
yB
zB
xD
yD

## Slide 8
Experimental Verification Using Vacuum Torsion Pendulum

## Slide 9: Original Measurement of Radiation Pressure using a Torsion Balance
P. Lebedew (1900)
University of Moscow
E. F. NICHOLS AND G. F. HULL (1901)
Dartmouth College
Both teams developed a similar torsion balance inside a chamber with the air evacuated.

## Slide 10: Recent Work with Radiation Pressure using a Torsion Pendulum
Chu et al. (2019)
Rochester Institute of Technology
Chandrasekar et al. (2025)
University of Michigan
Both teams drive their system at the natural frequency to amplify the system response.

## Slide 11: Proposed Method of Verifying DMD Control of SRP with Torsion Pendulum
Drive the Torsion Pendulum at the Operating Frequency
Pendulum Arm
  DMD Mounted at the furthest moment arm
  Wireless Microcontroller and Battery
  Self-contained within a Vacuum Chamber
Optical Lever
  The tracking laser reflected off a mirror at the pivot
  Displacement measured by Photodetector
Minimizing External Disturbances
  Lock-in Amplifier to match optical chopper with Photodetector
Demonstrate Closed-Loop control by both actively damping and amplifying pendulum response
Optical
Chopper
Microcontroller
Battery
Forcing
Laser
Tracking
Laser
4-Quadrant
Photodetector
Interpreter &
Transmitter
Lock-In
Amplifier
Torsion Wire Pivot
Mirror
Pendulum Arm
DMD System

## Slide 12
Parametric Design of Experimental Setup with System of Equations

## Slide 13: System of Equations and Initial Inputs
39 cm Diameter Vacuum Chamber
31 cm Height
10-5 Torr Vacuum Capable
ThorLabs MC2000B
4Hz-10kHz
0.1-0.5 Duty Cycle
Koheron 4-Quadrant Photodetector
8mm Diameter Target
We will endeavor to design the experiment to use the available equipment.
Vacuum Chamber
Optical Chopper
Photodetector

## Slide 14: Mechanical Considerations
Recent Work
Updated Work
A polymer pendulum arm allows heat sources to be isolated while the copper tape and aluminum fins move heat away from the heated components. Further refinement is necessary.
Bulk material AlSi10Mg with copper tape heat piping
41 grams
35 grams
Combining PEEK, Copper Tape, and Black Anodized Aluminum.

## Slide 15: Thermal Considerations
Recent Work
Updated Work
Measuring the components as they are intended to be used will further refine our predictions.
Grid Fins
Measuring Actual Thermal Output
  Bell Jar to low vacuum
  8x Thermocouples routed to components
  Multiple IR Cameras
Investigating Black Anodized Aluminum
  Anodize test aluminum samples
  Attempt to use Anodization Masking Tape for conductive surfaces
Improving DMD thermal interface
  Mill a copper block to fit DMD interface

## Slide 16: Digital Micromirror Device Selection
DMD | Diagonal (in.) | Max Vis. Illumination (W/cm2) | Typical Elect. Power (W) | Thermal Interface
DLP2000 | 0.20 | * | 0.045 | No
DLP160AP/CP | 0.16 | 26.1 | 0.07 | Yes
DLP2010 | 0.20 | 26.1 | 0.07 | No
DLP230GP/KP/NP | 0.23 | 26.1 | 0.17 | Yes
DLP3010 | 0.30 | 26.1 | 0.10 | Yes
DLP3310 | 0.33 | 26.1 | 0.16 | Yes
DLP4710 | 0.47 | 20.5 | 0.25 | Yes
DLP472TP | 0.47 | 20.5 | 1.0 | Yes
Commercially available DLP® Pico™
Examples of Thermal Interfaces
* Thermally Limited
DLP160CP
DLP160CP
DLP2000
DLP2000
The Pico DMD systems are effectively interchangeable, which accelerates design between systems.

## Slide 17: Wireless Microcontroller Selection
Microcontroller | Mass (g) | Typical Power (mW) | Typical Max Current (mA) | Interfaces |  | 
 |  |  |  | I2C | SPI | UART
Raspberry Pi Pico W | 4 | 238 | 150 | Yes | Yes | Yes
Adafruit Feather HUZZAH | 8 | 925 | 250 | Yes | Yes | No
Adafruit Feather Bluefruit | 7.4 | 96 | 26 | Yes | Yes | No
Adafruit QT Py Pico | 3.9 | 370 | 100 | Yes | Yes | Yes
Commercially available DLP® Pico™
RPi Pico W
HUZZAH
Bluefruit
QT Py
Experimenting with the different microcontrollers will help identify the minimum requirements.
WiFi Bluetooth

## Slide 18: Electrical Considerations
Configuration | Average Current (mA) | Peak Current (mA)
Initial Estimate | 177 | -
DLPC2000EVM | 232.24 | 270.61
DLP2000EVM + MCU* | 292.89 | 332.40
DLP2000EVM + MCU + LEDs OFF | 116.39 | 128.67
DLP2000EVM + MCU + LEDs OFF + Decreased Refresh Rate | 111.21 | 130.96
Replacing the Raspberry Pi Pico W will further reduce power requirements.
Event | Duration (min) | Electrical Capacity (mAh) | Average Current (mA)
Pump Down | 10 | 10.11 | 60.65*
Preparation | 1 | 1.85 | 111.21
Execution | 10 | 18.54 | 111.21
Shutdown | 1 | 1.85 | 111.21
Total Electrical Capacity | 32.35 mAh
Peak Operational Current | 130.96 mA
*Average current consumption of current MCU board. Value expected to be lower with differing MCU board selection
*MCU board used for analysis: Raspberry Pi Pico W
Vacuum Operational Estimates
Power Consumption Analysis
Possible savings by reducing pump down time by not requiring high vacuum conditions
Successfully able to reduce power consumption below initial estimates
60 Hz
1 Hz

## Slide 19: Areas for Further Work
Breakout
Boards
Narrow interfaces and define thermal and electrical requirements
Capable of 30 kbps one-way for only 3mA. Support deep sleep microcontroller operations.
LiPo battery meets power requirements for only 3 grams. Investigating reinforced epoxy resin.
Revisiting assumptions concerning using external power
Optical
Comms
LiPo
Battery
External
Power

## Slide 20: Questions? Suggestions?
jmesser@usc.edu
Upcoming Conferences
International Symposium on Space Sailing
July 1st Delft, NLD
ASCEND
July 22nd Las Vegas, NV
pastizzo@usc.edu

## Slide 21: Electrical Considerations
90 | 177
Event | Duration (min) | Electrical Capacity (mAh) | Max Current (mA)
Pump Down | 45 | 54 | 72
Preparation | 1 | 3 | 177
Execution | 10 | 30 | 177
Shutdown | 1 | 3 | 177
Function | Component | Average Current (mA)
DMD | DLP2000 | 30
DMD Controller | DLPC2607 | 63
PMIC | DLPA1000 | 12
Microcontroller | Raspberry Pi Pico W | 72
Initial Estimation
Updated Work
Saft LS 14500 HT (Li-SOCl₂)
2200 mAh & 100 mA
AA-Size & 17 g
Commanded via RPi Pico I2C
Average Current from 110mA to 55mA
Max Current from 105mA to 68mA
We are designing breakout boards to further identify opportunities to reduce power requirements.
Thank you, Joshua Pastizzo

## Slide 22: Solar Sailing Attitude Control of GEO Satellite (Lievre)
Derivations of this method are found on several GEO satellites
Fixed Solar Trim Tabs are attached to solar arrays. Solar Array Drive Actuator is used to create a torque bias about Roll and Yaw
  Does not provide Pitch control
  Control Torque 10-20x10-6 N⋅m
Requires Solar Arrays to be pivoted away from solar vector to generate torques
  Acceptable control with 1% loss of Solar Array Efficiency (Azor 1992)
(Liever, 1985)
(Sidi, 1997)
Yaw
Roll
For GEO satellites, Pitch continues to
require Momentum Dumping

## Slide 23: IKAROS Method
Launched in 2010 on Venus flyby
Employed a novel reflectance control device (RCD) for attitude control
  IKAROS was spun to deploy solar sail
  Flexible liquid crystal sheets were affixed to the perimeter of the solar sail
  The optical reflectivity of the RCD changed with the applied voltage
  Specular when ON and diffuse when OFF
The sequence of the RCD was synchronized with the satellite’s spin for fuel-free changes to the satellite’s spin axis
(T. Tsuda et al, 2011)
This propellant-free attitude control method still requires momentum-dumping fuel to maintain its Roll rate
(T. Tsuda et al, 2011)

## Slide 24: Evaluation for the Space Environment
Normal Operation MTBF >650,000 hours
  Individual hinge lifetime >3x1012 duty cycles
  Duty cycle patterns can effectively extend lifetime indefinitely
Testing conducted for Space-Based Multi-Object Spectroscopy
  Vibration and Shock
  Gamma Radiation
  Heavy Ion Irradiation
  Proton Radiation
  Cryogenic Temperatures (78K)
Space Environmental Testing indicated DMDs self-healed through annealing
COTS DMD 20.0 krad(Si)
Re-windowed DMD 20.0 krad(Si)
(Oram et al, 2019)
Gamma Radiation Exposure Testing
Heavy Ion Radiation Exposure Testing
(Travinsky et al, 2016)
18.6 krad(Si) Typical for L2 over a 4-year mission
Inherent Recovery from Single Event Upsets

## Slide 25: How does a DMD work?
The next micromirror tilt state is stored in the memory immediately beneath the micromirror.
A “mirror clocking pulse” is applied to the mirrors, flexing their spring tips attached to the yoke.
The bias voltage is turned off, releasing the mirrors from their latch.
Opposing electric fields are applied to the mirrors to rotationally separate the mirrors staying in their current state from those transitioning to a new state.
The bias voltage is turned back on to finish landing and latching the mirrors in their new state.
The memory is again updated for the next state, and the process repeats.
(Texas Instruments, 2024)
(Hornbeck, 1997)
Each micromirror is individually commanded and globally executed

## Slide 26: Initial Considerations for Assembling the System of Equations
Electrical
Thermal
Mechanical
Sufficient capacity for the duration of setup and experiment
Provide necessary maximum current
Safely operate inside a vacuum
Must quickly transfer heat away from heat sources
Must either store heat in pendulum arm or transfer heat into surroundings
Pendulum arm must operate within vacuum chamber
Displacement measurement must observe with sufficient sensitivity

## Slide 27: REFERENCES
1. Oram, K., Vorobiev, D., Ninkov, Z., "The effects of gamma radiation on digital micromirror devices," Vol. 10932, SPIE, 2019, pp. 109320V–12.
2. Lievre, J., "Solar Sailing Attitude Control of Large Geostationary Satellite," IFAC Proceedings Volumes, Vol. 18, No. 4, 1985, pp. 29–32.
3. Sidi, M.J., "Spacecraft Dynamics and Control: A Practical Engineering Approach," Cambridge University Press, 1997,
4. Ito, T., Ikari, S., Funase, R., "Active use of solar radiation pressure for angular momentum control of the PROCYON micro-spacecraft," Acta Astronautica, Vol. 152, 2018,
5. Scull, J., "Guidance and Control of the Mariner Planetary Spacecraft," IFAC Symposium on "Automatic Control in the Peaceful Uses of Space",
6. Kawaguchi, J., and Shirakawa, K., "A Fuel-Free Sun-Tracking Attitude Control Strategy And the Flight Results in Hayabusa (MUSES-C)," Advances in the Astronautical Sciences, Vol. 127, 2007, pp. 1989–1996.
7. Tsuda, Y., Saiki, T., Funase, R., "Generalized Attitude Model for Spinning Solar Sail Spacecraft," Journal of Guidance, Control, and Dynamics, Vol. 36, No. 4, 2013, pp. 967.
8. Travinsky, A., Vorobiev, D., Ninkov, Z., "Effects of heavy ion radiation on digital micromirror device performance," Optical Engineering, Vol. 55, No. 9, 2016,
9. FLAMENT, and PATRICK, "ATTITUDE CONTROL DEVICE USING SOLAR SAILS FOR A SATELLITE STABILIZED ON THREE AXES," No. US5133518A, 1992,
10. Goodzeit, N.E., and Ratan, S., "Spacecraft disturbance trimming system," No. 7104506, 2006,
11. Orphee, J., Diedrich, B., Stiltner, B., "Solar Sail Attitude Control System for the NASA Near Earth Asteroid Scout Mission," [online database]
12. Chu, Y.L., Tabiryan, N.V., and Swartzlander, G.A., "Experimental Verification of a Bigrating Beam Rider," Physical Review Letters, Vol. 123, No. 24, 2019,
13. Nichols, E.F., and Hull, G.F., "The Pressure Due to Radiation. (Second Paper.)," Physical Review (Series I), Vol. 17, No. 1, 1903, pp. 26–50.
14. Hornbeck, L.J., "Digital light processing for high-brightness high-resolution applications," Projection Displays III, Vol. 3013, SPIE, 1997, pp. 27–40.
15. Chandrasekar, K., Carman, A.E., Watts, R.M., "Characterization of a Sensitive Inverted Pendulum Thrust Stand for Pulsed Propulsion With Optical Heterodyne Sensor and Lock-In Detection," AIAA SCITECH 2025 Forum, American Institute of Aeronautics and Astronautics, 2025,
16. Lebedew, P., "Untersuchungen über die Druckkräfte des Lichtes," Annalen Der Physik, Vol. 311, No. 11, 1901, pp. 433–458.